## Slide 1: ENGI 301 “Loss Prevention Device” PCB Proposal
November 22, 2020
Spencer Wong

## Slide 2: Background Information
In project 01, I prototyped a “loss prevention device”, designed around a Pocket Beagle, Bluetooth, Wi-Fi, and GPS module. This device connects to your phone, and texts your phone once it leaves the Bluetooth range. The text is customizable, but mainly includes the coordinates of the device at the time of separation. This device can be used for keeping track of children, valuables, and more.
Notes: What is being proposed?
  Pictures
  Links to existing projects / libraries
What improvements / additions over existing project

## Slide 3: System Block Diagram
Pocketbeagle
UART4
TX
DSD TECH HM-10
RX
Smart Phone
Bluetooth
USB1
Internet Source (probably a WiFi adapter)
MicroUsb Power Source (Car charger, battery, etc)
MicroUSB
UART2
TX
RX
GT-U7
Notes: Create a System Block Diagram
  Label interfaces / pins
  Components (part numbers if possible)

## Slide 4: Power Block Diagram
Pocketbeagle
DSD TECH HM-10
Vout
5 Volts
Internet Source (probably a WiFi adapter)
USB1
MicroUsb Power Source (Car charger, battery, etc)
MicroUSB
GT-U7
Notes: Create a Power Block Diagram
  Label voltages / currents of components

## Slide 5: Mechanical Block Diagram
FRONT
BACK
2”
2.5”
Pocket Beagle
USB/Wi-Fi
GPS
BT
USB
Note: The BT module’s pins are sideways
~1”
~1”
~0.8”
~0.8”
~1.7”